## Slide 1: Sustainability Assurance Modeling for SRAM-based FPGA Evolutionary Self-Repair
11 December 2014
Rashad S. Oreifej, Rawad Al-Haddad,
Rizwan A. Ashraf, and Ronald F. DeMara
Department of Electrical Engineering and Computer Science
University of Central Florida

## Slide 2: “Beyond Redundancy”
  Fault Avoidance: “Always Possible?” No
  Design Margin: “Always Adequate?” No
  Modular Redundancy: “Always Recoverable?” No
  Autonomous Refurbishment: “Highly Flexible?”
  Yes … but how to achieve???

unforeseen events
restricted human intervention
X
X
X
Embedded Fault-Handling
Not Sustainable
Not
Scalable
Granularity
core
module
CLB
gate
transistor
Evolvable
Hardware
Static
Redundancy
Adaptation
none
routing
on-demand
In-situ
Resynthesis
LUT
unconstrained
LUT-level Granularity
On-demand Adaptation
Goal: How many reconfigurable resources are needed to sustain functionality using evolution?

## Slide 3: Role of Sustainability
Billions of
Transistors
local permanent damage
aging
effects
intra-die variations
manufacturing defects
“How can an embedded system sustain itself …
to achieve lifetime mission specifications
despite multiple unforeseeable faults
within failure-prone environments
using a large number of unreliable components ?”
Sustainability:
how well a system endures over lifetime by utilizing available resources
a system is sustainable if it maintains its net refurbishment ≥ net failure
FPGA LUT is selected as unit of reconfigurability
 “Amorphous spare resource”
“autonomy”
Notes: 3

## Slide 4: Modeling Approach Probabilistic Model based on EHW repair statistics
 | Combinatorial Modeling | State-space Modeling | This Approach
Method | Map system into fixed structure or network | State transition graphs | Topology-independent probabilistic model
Analysis Method | Qualitative  min-cut analysis (or) Quantitative  probabilistic evaluation | Quantitative  probabilistic evaluation | Quantitative  probabilistic evaluation
Computation Complexity | High | High | Low
Analysis Granularity | Coarse Grained: Subsystem – level | Coarse Grained: System / subsystem – level | Fine Grained: Component – level
Support Design Reconfigurability | No | Low | Yes: amorphous
Precision | Exact | Exact / Approximated | Approximated
Scalability | Low | Low | High
Scope | Reliability | Reliability | Sustainability

## Slide 5: Sustainability Modeling Using amorphous spares to meet mission objectives
Quantitative stochastic model for FPGA-based reparable systems
Estimates reconfigurable resources required for refurbishment to meet mission availability and lifetime in a given fault types, rates, and impact model
Method: no Topology information / State-Transition Graphs
Complexity: computational complexity is low as compared to Combinatorial modeling
Precision/Scalability: precision is approximate but scalability is high as compared to conventional methods

## Slide 6: Sustainability Modeling Model parameters for EHW
Amorphous Spares available at runtime depends on the design-time allocation:
Resource Consumption Rate
Number of Resources Consumed for system recovery up until time t:
Affected resources depends on Fault Rate
Sustainable if and only if the ratio is satisfied:
Probability Density Function for Faults
Availability lower bound to meet mission requirements under failure rates:
Time Dependent Dielectric Breakdown
Electromigration

## Slide 7: Analytical Model Example mechanisms of autonomous recovery
Resource Recycling
Fault impact can vary
Not all impacted LUTs are unusable
GA can leverage partially functional resources
Fault cost model can be adjusted according to GA statistical data

## Slide 8: Sustainability Model Application
Use-case
  MCNC circuit benchmark set
  Sobel Edge detection payload on NASA Messenger mission
Repair Policy
  GA-based evolutionary repair
  Circuits partitioned into tiles with local CED
  A C++ simulator was built to evaluate the GA convergence time for a tile of 40-LUTs with under cumulative faults
  GA convergence time is translated from simulation generations into intrinsic evolution time by coefficients obtained using EHW repair
  Arena discrete simulation model was developed for each MCNC benchmark to evaluate the reparability decay based on GA simulations
Fault Models
  Permanent faults (TDDB and EM)  aging-induced
  Failure rates consolidated from those reported in literature and vetted device datasheets

## Slide 9: MCNC Benchmarks Sustainability Analysis: 100% QOR
Simplex
Adaptive TMR
Higher Lifetime predicted with Adaptive TMR
High Amorphous Resource Pool (ARP) size required with Adaptive TMR
Resource constrained
QOR: 100%
QOR: 100%
QOR: 100%
QOR: 100%
Notes: Based on given availability thresholds for mission, the max lifetime possible is calculated by using the model. Then it is used to calculate a lower bound on amorphous spares required to get the determined lifetime.
a) Relaxing the availability threshold, more lifetime…
b) missions with smaller designs are sustainable for longer periods
c) More lifetime possible with Adaptive TMR (at expense of area and power), furthermore, it requires a larger amorphous resource pool in order to keep all three modules online.

## Slide 10: MCNC Benchmarks Sustainability Analysis: 95% QOR
High-Longevity
High-Availability
with Adaptive TMR
# Faults | Ave. # Generations 95% Fitness | Ave. # Generations 100% Fitness | % of the GA Runtime to evolve 95% Fitness | # Runs
1 | 114 | 3962 | 2.88% | 100
2 | 1230 | 31352 | 3.92% | 50
3 | 3920 | 38601 | 10.16% | 50
4 | 9238 | 63307 | 14.59% | 30
5 | 11958 | 88746 | 13.47% | Interpolated
6 | 19527 | 133248 | 14.65% | Interpolated
7 | 31887 | 200066 | 15.94% | Interpolated
8 | 51981 | 290643 | 17.88% | 10
Simplex
Adaptive TMR
QOR: 95%
QOR: 95%

## Slide 11: NASA MESSENGER Sobel-Edge Detector Sustainability
Sobel Edge-Detector with ARP-based GA Sustainability Results (Conservative) |  |  |  |  |  |  | 
λTDDB=1%, λEM=0.2% Time unit: years |  |  |  |  |  |  | 
Constant Model Inputs | Variable Model Inputs |  |  |  | Sustainable | Ravail (LUT) | Tmax
 | QOR | MTTRTDDB(t) | MTTREM(t) | AvailThr |  |  | 
T = 8 MTTFTDDB=0.17 MTTFEM=0.83 Rd=600 LUT/FE | 100% | 6.4E-4e0.156t | 6.4E-4e0.032t | 99.99% | × | 53 | 2.71
 |  |  |  | 99.9% |  | 231 | 10.9
 | 95% | 6.5E-5e0. 183t | 6.5E-5e0. 037t | 99.99% |  | 289 | 13.27
Sobel Edge-Detector with ARP-based GA Sustainability Results (Pessimistic) |  |  |  |  |  |  | 
λTDDB=5%, λEM=0.4% Time unit: years |  |  |  |  |  |  | 
Constant Model Inputs | Variable Model Inputs |  |  |  | Sustainable | Ravail (LUT) | Tmax
 | QOR | MTTRTDDB(t) | MTTREM(t) | AvailThr |  |  | 
T = 8 MTTFTDDB=0.03 MTTFEM=0.42 Rd=600 LUT/FE | 100% | 6.4E-4e0.782t | 6.4E-4e0.063t | 99.6% | × | 61 | 0.60
 |  |  |  | 90% | × | 423 | 3.52
 |  |  |  | 80% | × | 520 | 4.15
 |  |  |  | 50% | × | 722 | 5.30
 | 95% | 6.5E-5e0.729t | 6.5E-5e0.073t | 99.6% | × | 356 | 3.05
 |  |  |  | 90% | × | 761 | 5.5
 |  |  |  | 50% |  | 1415 | 8.15
significant amorphous pool for 50%
if “4 nines” required then provide 289 LUTs
or for “3 nines” provide 231 LUTs for 100% QOR
if availability < 50% then system spends more of mission offline than online
Notes: Given some model inputs like the max mission lifetime (T) DESIRED, the failure rates lambda expected (means) and Rd Resource actually utilized by the design:
Then based on desired QOR, find the Tmax possible. If Tmax possible is less than T, then mission is not sustainable. Now given same parameters estimate the amorphous spares required to make the mission sustainable. Eg. In table top, if amorphous spare pool is increased to 231 it is possible to have 10.9 Years and hence make the mission sustainable.
Table below is pessimistic case where failure rates are too high and it is shown that sustainability is only possible with low availability requirement and huge number of resources.

## Slide 12
NASA MESSENGER
Sobel-Edge Detector Sustainability
Mission Sustained:
T = 8 years
Availthr = 99.9%
QOR = 100%
ARP = 190 resources
Power Savings = 31% TMR
Mission Sustained:
T = 8 years
Availthr = 55%
QOR = 95%
ARP = 1370 resources
Power Savings = 25% TMR
Conservative case
Pessimistic case
Notes: The Availability degradation and ARP resources consumed (red curve) during the 8-year Messenger mission with the hypothetical Sobel Edge-detector. Future Work: Routing restrictions may be addressed through variable Repair Cost (which may be highly non-linear)
For QOR of 95%, which is equivalent to 3k bad pixels in an edge detected frame of 65k-pixels
You can mention achievable power savings under pessimistic and conservative cases determined by time spent in TMR mode vs CED which is affected by availability.

## Slide 13
 | Resources available for refurbishment (design-time) ≥ Resources needed for repair (run-time)
 | Probabilistic estimate of Rc
 | Sustainability Test Ratio (STR)
 | Design STR
 | Mission Faulty Resource Density
 | Availability Threshold vs. Mission Duration
 | Solve polynomial for Tmax for a given Availmax

C1 = MTTRTDDB0,
X1 = αTDDB* λTDDB,
Y1 = MTTFTDDB,
C2 = MTTREM0,
X2 = αEM* λEM,
Y2 = MTTFEM,
More details in Manuscript …
Analytical Model

## Slide 14
Questions?

## Slide 15
BACKUP SLIDES …

## Slide 16
1. Initialization: obtain configuration from .bit | 3. Fitness Evaluation: performed in two phases | 
 | FPGA Reconfiguration | Pattern Evaluation
2. GA Operations: derive new individuals |  | 
START: module-based flow
Iterate: frame-based flow
Intrinsic Evolution Workflow

## Slide 17
The developed platform consists of following software components:
GA Engine
  C++ based console application implemented using an object oriented architecture
  Implements a conventional population-based GA with runtime customizable parameters
Chromosome Manipulator
  C based GA operators library (yet executed using Visual Studio .NET)
  Provides a logical abstraction and hardware transparency of genetic operators to the GA Engine module (SPX, PMX, OX, CX, Mutation)
MRRA
  Partitions operations into Logic, Translation, and Reconfiguration layers with a standardized set of APIs
  FPGA configurations are manipulated at runtime using on-chip resources on Xilinx Virtex II Pro via PC (JTAG) or PowerPC (SelectMAP)
Bitstream File
  Pre-compiled baseline bitstream generated using the Xilinx CAD tools
  The platform manipulates this bitstream to carry out the physical mapping of the crossover or mutation
Intrinsic Evolution Workflow

## Slide 18: SRAM-Based FPGA Fault Characteristics
Cat. | Type | Cause |  | Affected Resources | Volatility | Refurbish
 |  | Source | Description |  |  | 
Soft | Soft | Radiation | SEU (high-energy particle “proton, neutrons, alpha, heavy ion” striking a storage element) | Design flops and memory | Trans. | Not needed
 | Firm | Radiation | SEU | Config. mem (95% of memory elements incl. BRAM is config.) | Semi-perm. | Scrubbing
 | Tough | Radiation | SEU | Reconfiguration Circuitry | Persistent | Pwr-on-rst
Hard | Manufac. | Infant Mortality | Process Imperfections | All | Perm. | Mask out
 | TID | Radiation | Change switching char. | LUT, IOBs, FF | Perm. | Avoid
 | TDDB | Aging | Electrons trapped in imperfections of the oxide well enough to create very low resistive path “short circuit” at the transistor gate | LUT, IOBs, FF | Perm. | Avoid
 | EM | Aging | Electron depletion in very thin wires with increased temp. creates a highly resistive path | Interconnect | Perm. | Avoid
 | HCE | Aging | Traps at oxide surface, change of VTh of transistors | LUT, IOBs, Mem | Perm. | Avoid in Critical Path
 | NBTI | Aging | Temperature distribution, PAR dependent | LUT, IOBs, Mem | Perm. | Avoid in Critical Path

## Slide 19: In Paper: Mission Sustainability Analytical Model
Definitions:
Quantity | Description | Unit
f(t): | PDF - Fault probability distribution density as a function of time. Whether the fault distribution follows linear, Poisson, normal, Gaussian, binomial, hypergeometric, …, etc distribution, it is a major factor that can highly affect the system sustainability. | Dimensionless 0 ≤ f(t ) ≤ 1
Ci: | Cost in terms of number of resources spent on recovering from a fault of the type (i). For example if there are two types of faults considered: 1. stuck-at-one and 2. stuck-at-zero, then the cost to recover from the stuck-at-one fault is denoted by C1 and the cost to recover from the stuck-at-zero fault is denoted by C2 Different faults entail different resource damage patterns and therefore require different number of resources to recover from depending on the fault impact and location. TBD: Normally Ci = 1 if no tiling is considered in the repair process. If tiling is considered “i.e. resources are organized in spatial groups called tiles and when a resource within a tile becomes faulty the entire tile is replace by a spare one, then Ci = 1 tile or Ci = Size(tile).” | Unit Resource
Rc(t): | Resource consumption as function of time. This quantity represents the number of resources consumed for fault recovery at any instance of time. | Unit Resource
Ravail(t): | Resources available for repair as function of time. | Unit Resource
T: | System anticipated target lifetime. | Unit Time
Rep(t): | System reparability which refers to the capability of the fault-tolerant-System to repair itself and recover from a fault. Reparability degrades exponentially by time as the system undergoes faults during its operational lifetime. | 

## Slide 20: Device Degradation
Aging-induced progressive during mission
  Electromigration
  • conductors at increased temperatures morph due to high current density: opens/shorts
  Time-Dependent Dielectric Breakdown (TDDB)
  • oxide layer insulator properties breakdown due to electric field exposure: RGC
  Bias Temperature Instability (BTI)
  • dangling bonds at Si-SiO2 interface form interface traps in channel,
  interface traps become progressively occupied by carriers: Vth
  Thermal Cycling
  • bulk heating/cooling of chip/package: intermittent or permanent faults
Radiation-induced spontaneous during mission
  Single Event Upset (SEU)
  • “Soft Errors”: alpha particle collision creates electron-hole pair in substrate,
  charge collected at device terminals may upset logic state
  Single Event Latchup (SEL)
  • local permanent damage from highly energetic single burst
  Total Ionizing Dose (TID)
    • cumulative damage due to lifetime radiation exposure